NODEMCU ESP 8266
JAYANT RAJWANI
+91-8885444431

---
Internet Pops Up here :D
What is IoT?
Prototyping electronics for IoT
How to connect?
IoT with Blynk and ESP8266

---
Internet of Things
Internet of Things
”IoT is a network of physical objects with embedded electronics that collect and share data”

---
Components for IoT
Components for IoT
- ESP8266 module
- NodeMCU 1.0
- Arduino UNO wifi Shield
- OTA WeMos D1

---
ESP8266 module
ESP8266 module
- We are using this today
- Can be programmed by itself but usually connected to Arduino
- Price: 2 – 5 €

---
ESP8266 module pinout
ESP8266 module pinout

---
NodeMCU 1.0
NodeMCU 1.0
- Built-in ESP8266, ”ESPduino”
- Works with Arduino IDE, not officially though
- 12 V regulator for input voltage
- Price: 5 – 10 €
- 13 GPIO, only one PWM and ADC (0-1 V)
Pins work with 0 - 3,3 V!

---
NodeMCU 1.0 Pinout
NodeMCU 1.0 Pinout

---
http://arduino.esp8266.com/stable/package_esp8266com_index.json
- File > Prefereences
- Paste above link in Additional Board
  Manage Url's
- Click Ok
- Tools > Boards > Boards Manager
- Select the last option ESP8266 and click install that appears there.

---
Pin Numbers for NODEMCU
in
Arduino

---
Installing Blynk libraries
Installing Blynk libraries
1. http://www.blynk.cc/getting-started/
2. https://github.com/blynkkk/blynk-library/releases/tag/v0.3.1
Download the Blynk_v0.3.1.zip in the bottom of the page

---
Extracting libraries
Extracting libraries
Extract the 4 folders inside the .zip to: C:\Program Files (x86)\Arduino\libraries
Done!

---
Blynk for phone
Blynk for phone
- Download the app for your phone
- You will get a project code to your e-mail
  - You need to copy paste it to your Arduino Code

---
How to connect Arduino?
How to connect Arduino?

---
Code for Arduino
Code for Arduino
In the end of the presentation there is the code in text format

---
ESP8266 after Blynk
ESP8266 after Blynk
- Using the ESP8266 without an app like Blynk requires some coding skills, although lots of ready-made code can be found on the internet.
- You can connect with the module directly within its range or anywhere through internet.
- For internet connection you’ll need a website to which the module sends data or where you can send data to the module.
- A good basic example project can be found here http://allaboutee.com/2015/01/02/esp8266-arduino-led-control-from-webpage/ In this example you have a webpage with buttons that control LEDs connected to an Arduino with an ESP module.
- The module acts as a serial device, and you speak to it through AT commands.
  - For example AT+CWLAP gives a list of the available access points (Wi-Fi networks). A list of commands can be found here: https://nurdspace.nl/ESP8266#AT_Commands

---
Resources
Resources
• Google & Youtube - search for projects, solutions to occurring problems
and data sheets for components
• http://www.blynk.cc/ - Homepage of the Blynk software, getting started,
community forums
• http://www.esp8266.com/ - Everything on ESP8266, wiki
• https://www.adafruit.com/ - Learning materials, guides, example projects,
forums, store
• https://github.com/ - Largest code host, lots of projects and sample code
• http://allaboutee.com/ - good ESP8266 tutorials
• https://nurdspace.nl/ESP8266/ - ESP8266 info and basic list of AT
commands

---
#define BLYNK_PRINT Serial // Comment this out to disable prints and save space
#include <ESP8266_SoftSer.h>
#include <BlynkSimpleShieldEsp8266_SoftSer.h>
#include <SimpleTimer.h>
// Set ESP8266 Serial object
#include <SoftwareSerial.h>
SoftwareSerial EspSerial(2, 3); // RX, TX
ESP8266 wifi(EspSerial);
// You should get Auth Token in the Blynk App.
// Go to the Project Settings (nut icon).
char auth[] = "your_auth_token";
float temp;
int tempPin = 1; //analog pin 1
int reading;
float voltage;
SimpleTimer timer;
void setup()
{
// Set console baud rate
Serial.begin(9600);
delay(10);
// Set ESP8266 baud rate
// 9600 is recommended for Software Serial
EspSerial.begin(9600);
delay(10);
Blynk.begin(auth, wifi, "ssid", "password"); // enter wifi name and password to it
timer.setInterval(1000L, sendTemperature);
}

---
// This function sends the value of "temp" every second to Virtual Pin (5).
// In the app, Widget's reading frequency should be set to PUSH. This means
// that you define how often to send data to Blynk App. This function is used (instead of
// sending data in the loop function) to avoid over-loading the Blynk servers.
void sendTemperature()
{
// You can send any value at any time.
// Please don't send more that 10 values per second as this will cause a flood error.
Blynk.virtualWrite(V5, temp);
}
void loop()
{
Blynk.run(); // Initiates Blynk
timer.run(); // Initiates SimpleTimer
// This changes the analog pin reading to Celsius degrees,
// which is then sent to Blynk in the SendTemperature function.
reading = analogRead(tempPin);
voltage = reading * 5;
voltage /= 1024;
temp = (voltage-0.5)*100;
}