Introduction to...
Arduino
Introduction to...
Arduino
[Speaker Notes: This presentation demonstrates the new capabilities of PowerPoint and it is best viewed in Slide Show. These slides are designed to give you great ideas for the presentations you’ll create in PowerPoint 2010! For more sample templates, click the File tab, and then on the New tab, click Sample Templates.]

---
Contents:
What is Micro-Controller?
What is Arduino?
Types of Arduino.
Arduino UNO board.
Sensors:
- Digital, Analog sensors.
- Light sensors [IR sensor, Photo-Resistor].
Coding structure and examples
Data types and operators.
What is “Function”?
Control statements [if, if… else, switch case.].
Loop statements[while, for, do… while.].
Common functions.

---
Introduction
1
Introduction

---
Micro-Controller:
Micro-Controller:
It is a micro-computer. As any computer it has internal CPU, RAM, IOs interface.
It is used for control purposes, and for data analysis.
Famous microcontroller manufacturers are MicroChip, Atmel, Intel, Analog devices, and more.

---
What is Arduino?
A microcontroller board, contains on-board power supply, USB
port to communicate with PC, and an Atmel microcontroller
chip.
It simplify the process of creating any control system by
providing the standard board that can be programmed and
connected to the system without the need to any sophisticated
PCB design and implementation.
It is an open source hardware, any one can get the details of its
design and modify it or make his own one himself.
Arduino.

---
Arduino boards:
Arduino boards:
UNO
Mega
LilyPad
Arduino BT
Arduino Nano
Arduino Mini

---
Arduino UNO:
Arduino UNO:
Digital output
~: PWM.
0,1: Serial port.
In circuit Serial programming
Atmel MicroController
USB port
Power input
Analog input.
Power Supply

---
Digital or Analog?
All physical quantities are analog.
Analog means that the quantity can take any value between its
minimum value and maximum value.
Digital means that the quantity can take specific levels of values
with specific offset between each other.
Ex: 1- Digital:
English alpha consists of 26 letter, there is no letter between A
and B.
- Square waves are Digital.
Ex.: 2- Analog:
Temperature, can take any value[-1,12.8,25.002,… etc.].
- Sine waves are analog.
Digital and analog.

---
Sensors:
A device that transforms the physical quantity into electrical
value.
Ex.: Light sensor transduce the light into change in voltage or
resistance.
Sensors

---
Light sensors:
Photo-Resistor [photo-cell].
Photo-Diode.
Photo-Transistor.
Sensors
[Speaker Notes: http://hades.mech.northwestern.edu/index.php/Optoreflector http://hades.mech.northwestern.edu/index.php/Optointerrupter]

---
Arduino Coding.
2
Arduino Coding.

---
Data Types and operators
Data Types and operators
Integer: used with integer variables with value between 2147483647 and -2147483647.
Ex: int x=1200;
Character: used with single character, represent value from -127 to 128.
Ex. char c=‘r’;
Long: Long variables are extended size variables for number storage, and store 32 bits (4 bytes), from -2,147,483,648 to 2,147,483,647.
Ex. long u=199203;
Floating-point numbers can be as large as 3.4028235E+38 and as low as -3.4028235E+38. They are stored as 32 bits (4 bytes) of information.
Ex. float num=1.291;	[The same as double type]
You may need to know about these typed: Array, Boolean, byte, etc. here.

---
Statement and operators:
Statement and operators:
Statement represents a command, it ends with ;
Ex:
int x;
x=13;
Operators are symbols that used to indicate a specific function:
- Math operators: [+,-,*,/,%,^]
- Logic operators: [==, !=, &&, ||]
- Comparison operators: [==, >, <, !=, <=, >=]
Syntax:
; Semicolon, {}	curly braces, //single line comment, /*Multi-line comments*/

---
Statement and operators:
Statement and operators:
Compound Operators:
++ (increment)
-- (decrement)
+= (compound addition)
-= (compound subtraction)
*= (compound multiplication)
/= (compound division)

---
Control statements:
Control statements:
If Conditioning:
if(condition)
{
statements-1;
…
Statement-N;
}
else if(condition2)
{
Statements;
}
Else{statements;}

---
Control statements:
Control statements:
Switch case:
 switch (var) {
    case 1:
      //do something when var equals 1
      break;
    case 2:
      //do something when var equals 2
      break;
    default:
      // if nothing else matches, do the default
      // default is optional
  }

---
Loop statements:
Loop statements:
Do… while:
do
{
Statements;
}
while(condition);	// the statements are run at least once.
While:
While(condition)
{statements;}
for
for (int i=0; i <= val; i++){
      statements;
   }
Use break statement to stop the loop whenever needed.

---
Code structure:
Code structure:
Void setup(){}
Used to indicate the initial values of system on starting.
Void loop(){}
Contains the statements that will run whenever the system is powered after setup.

---
Arduino IDE:
Arduino IDE:
You can download the Arduino IDE (The program used to write code and uploading it to arduino boards) from:
http://arduino.cc/en/Main/Software